## Slide 1: Report Writing
Representing Data with Excel

## Slide 2: Aims of Activity
To produce a high quality graph from experimental data using Excel.
To add linear trendlines to a graph using Excel.
To add error bars to a graph using Excel.

## Slide 3
Good Graphs
Title | Trendline
Data Spread | Equation and R2
Axis Labelled (including units) | Predicted and Measured Results
Appropriate Variables | Uncertainty Error Bars
When producing an experimental graph it is useful to consider the following checklist
We will cover how to produce a graph with all of these elements in todays computer lab.

## Slide 4
The Graph has a title.
Axis are labelled and have appropriate units.
Good Graphs

## Slide 5
The data is spread out over the entire graph.
Appropriate variables are plotted on the x and y axis.
Good Graphs

## Slide 6
Predicted and measured results are shown.
Uncertainty error bars are shown.
Good Graphs

## Slide 7
A trendline has been plotted.
The equation and R2 value of the trendline are shown.
Good Graphs

## Slide 8: Introduction
We will examine data from the simple experiment shown below.
Different masses, are attached to mass, and the acceleration, , is measured.

## Slide 9: Introduction
Where m 1(100 g) is the mass of the vehicle.
m2 is the mass of the falling weight.
a is the acceleration.
g is the gravitational constant.
Using Newton’s laws we can obtain the relationship between acceleration, , and the mass,

## Slide 10: Introduction
We then compare our equation to the standard equation for a straight line
Plot on the y-axis
Plot on the x-axis

## Slide 11: Part 1
Representing Data with Excel:
Producing a Good Graph

## Slide 12
Lets first look at how to produce a good graph
Part 1 – Producing a Good Graph

## Slide 13: Highlight the data you wish to include (both x values and the measured and predicted y values)
Part 1 – Producing a Good Graph

## Slide 14: Select the Insert tab from the top menu
Then choose Scatter
Part 1 – Producing a Good Graph

## Slide 15: Next click on the chart, then right click and select Move Chart in the menu.
Part 1 – Producing a Good Graph

## Slide 16: In the move chart window select New sheet. Then change the name to “Graph” and click on Ok.
Part 1 – Producing a Good Graph

## Slide 17: Highlight “Chart Title”, delete this text and type in the new the title of the graph;
“Acceleration versus Mass Ratio”
Part 1 – Producing a Good Graph

## Slide 18: Left click any number on the x-axis, and then right click, selecting format axis from the menu.
Part 1 – Producing a Good Graph

## Slide 19: Click on Fill & Line in the Format Axis menu.
Part 1 – Producing a Good Graph

## Slide 20: Select Line and set the line colour to black and adjust the Width to 3 and. Repeat the process for the y-axis.
Part 1 – Producing a Good Graph

## Slide 21: Left click on any number on x-axis, select the Home tab and adjust the font size to 20. Repeat for the y-axis.
Part 1 – Producing a Good Graph

## Slide 22: Left click on the graph title and set the font size to 24.
Part 1 – Producing a Good Graph

## Slide 23: Click Chart Design > Add Chart Element > Axis Titles > Primary Horizontal
Part 1 – Producing a Good Graph

## Slide 24: Click Chart Design > Add Chart Element > Axis Titles > Primary Vertical
Part 1 – Producing a Good Graph

## Slide 25: Copy and paste “m2/(m1+m2)” in to the x-axis title and “Acceleration (m∙s-2)” in to the y-axis title.
Part 1 – Producing a Good Graph

## Slide 26: Left click on the x-axis title and increase the font size to 20. Do the same for the y-axis title. You may find you need to shrink the main graph at this point.
Part 1 – Producing a Good Graph

## Slide 27: Highlight the “-2”, right click and select Font from the menu.
Part 1 – Producing a Good Graph

## Slide 28: Select superscript from the option box and click OK.
Part 1 – Producing a Good Graph

## Slide 29: Now repeat this process for each of the numbers in the x-axis label. Except instead of superscript, click on subscript.
Part 1 – Producing a Good Graph

## Slide 30: The graph should now look like this
Part 1 – Producing a Good Graph

## Slide 31: Click on one of the predicted values (red values), now right click and choose format data series from the menu.
Part 1 – Producing a Good Graph

## Slide 32: From the menu on the right side of the screen click on fill & line Then click on marker
Part 1 – Producing a Good Graph

## Slide 33: Next click on the marker options tab
Now choose the triangle symbol from the drop down menu
Part 1 – Producing a Good Graph

## Slide 34: To finish off the graph, left click on the x-axis and choose Axis Options form the right hand menu.
Part 1 – Producing a Good Graph

## Slide 35: Set the Minimum Bound to 0.30
Part 1 – Producing a Good Graph

## Slide 36: Now expand the Tick Marks menu
Part 1 – Producing a Good Graph

## Slide 37: Set the Major Type to Outside
Part 1 – Producing a Good Graph

## Slide 38: Repeat for the previous steps for the y-axis, set the Minimum Bound to 3.0 and add the Major Type Tick Marks to Outside
Part 1 – Producing a Good Graph

## Slide 39
This completes the first task and your graph should look like the example below.
Part 1 – Producing a Good Graph

## Slide 40
Good Graph Checklist
Title | Trendline
Data Spread | Equation and R2
Axis Labelled (including units) | Predicted and Measured Results
Appropriate Variables | Uncertainty Error Bars
We have now covered the following areas
X
X
X

## Slide 41: Part 2
Representing Data with Excel:
Linear Trendlines

## Slide 42
Lets add the trendlines (line of best fit) to the sets of data
Part 2 – Linear Trendlines

## Slide 43: Make sure your graph looks like the one below before you start to add the trendlines
Part 2 – Linear Trendlines

## Slide 44: Right click over any data point from the measured data. From the menu select Add Trendline.
Part 2 – Linear Trendlines

## Slide 45: Select Linear from Trendline Options and select the “Display Equation on chart” & “Display R-squared value on chart”.
Part 2 – Linear Trendlines

## Slide 46: Now do the same for the predicted values (red data points). Note we don’t include R-sqaured for the predicted data set as it should be 1. Your graph should now look like this.
Part 2 – Linear Trendlines

## Slide 47: Next drag and drop the equations into the relevant region (see below) and increase the font size of the equations to 18.
Part 2 – Linear Trendlines

## Slide 48: Finally left click on the predicted (red) trendline and select “Fill & line”
Part 2 – Linear Trendlines

## Slide 49: From the drop-down menu choose solid line type
Part 2 – Linear Trendlines

## Slide 50
This completes task two.
Part 2 – Linear Trendlines

## Slide 51
Good Graph Checklist
Title | Trendline
Data Spread | Equation and R2
Axis Labelled (including units) | Predicted and Measured Results
Appropriate Variables | Uncertainty Error Bars
When producing an experimental graph it is useful to consider the following checklist
We will cover how to produce a graph with all of these elements in todays computer lab.
X

## Slide 52: Part 3
Representing Data with Excel:
Error Bars

## Slide 53: Let’s add the uncertainty error bars.
Part 3 – Error Bars

## Slide 54: Make sure your graph looks like the one below for you start this task
Part 3 – Error Bars

## Slide 55: Left click on the a-measured data set. In the toolbar click Chart Design > Add Chart Element > Error Bars> More error Bars Options.
Part 3 – Error Bars

## Slide 56: Left click and then right click the x-error bars, and choose the delete option from the menu
Part 3 – Error Bars

## Slide 57: Left click on the y error bars, and select Error Bar Options from the righthand menu
Part 3 – Error Bars

## Slide 58: Click Custom, and then click on the Specify Value to give a new window: Custom Error Bars
Part 3 – Error Bars

## Slide 59
Click on the arrow of the Positive Error Value on the new window
Part 3 – Error Bars

## Slide 60: Go to the Data sheet, and highlight the standard uncertainty δam
Part 3 – Error Bars

## Slide 61: After you select the data the “Custom Error Bars” window should look like this
Now click on the arrow again
Part 3 – Error Bars

## Slide 62: Click on the arrow of the Negative Error Bars on the new window and repeat the process, again choosing the values under δam
Part 3 – Error Bars

## Slide 63: Go back to the Custom Error Bars window and click OK.
Part 3 – Error Bars

## Slide 64: The graph should now look like this:
Part 3 – Error Bars

## Slide 65: Now repeat the same process with the predicted data. When choosing the values to use for the error bars you should choose the following for the positive and negative values.
Part 3 – Error Bars

## Slide 66: The graph is now complete and can be used for you report.
Part 3 – Error Bars

## Slide 67
Good Graph Checklist
Title | Trendline
Data Spread | Equation and R2
Axis Labelled (including units) | Predicted and Measured Results
Appropriate Variables | Uncertainty Error Bars
When producing an experimental graph it is useful to consider the following checklist
We will cover how to produce a graph with all of these elements in todays computer lab.